## Slide 1: ECE2050 Digital Logic and Systems Tutorial 2
Huaiyu Li
223010059@link.cuhk.edu.cn
2025.02

## Slide 2: Decimal to Binary Conversion
Two methods:
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  Method 2: Repeatedly divide by 2, remainder goes in next most significant bit

## Slide 3: Decimal to Binary Conversion
Q1:
Convert 5310 to binary.
Method 1: Find the largest power of 2 that fits, subtract and repeat
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit

## Slide 4
A1:
Method 1: Find the largest power of 2 that fits, subtract and repeat
5310
53-32 = 21
21-16 = 5
5-4 = 1
32×1
16×1
4×1
1×1
= 1101012
Decimal to Binary Conversion

## Slide 5
A1:
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
5310 =
53/2 = 26 R1
26/2 = 13 R0
13/2 = 6 R1
6/2 = 3 R0
3/2 = 1 R1
1/2 = 0 R1
= 1101012
Decimal to Binary Conversion

## Slide 6: Two’s Complement Numbers
Q2:
Reverse the sign of 610 = 01102, Represent the result in two's complement form.

## Slide 7: Two’s Complement Numbers
A2:
Reverse the sign of 6 = 0110, Represent the result in two's complement form.
1. 1001
2. + 1
10102 = -610

## Slide 8: Two’s Complement Examples
Q3:
What is the decimal value of the two’s complement number
10012?

## Slide 9: Two’s Complement Examples
A3:
What is the decimal value of the two’s complement number 10012?
1. 0110
2. + 1
01112 = 710, so 10012 = -710

## Slide 10: Subtraction with Signed Numbers
Q4:
3 – 5 =

## Slide 11: Subtraction with Signed Numbers
A4:
1. 3 – 5 = 3 + (-5)
2. 0011 | 3
+ 1011 | -5
1110 | -2

## Slide 12: Binary Coded Decimal (BCD)
Q5:
In a binary coded decimal (BCD) system, 4 bits are used to represent
a decimal digit from 0 to 9. For example, 37 is written as 00110111BCD.
Write 371 in BCD.
Convert 000110000111BCD to decimal.
Convert 10010101BCD to binary.

## Slide 13: Binary Coded Decimal (BCD)
A5:
Write 371 in BCD.
  0011 0111 0001
Convert 000110000111BCD to decimal.
  187
Convert 10010101BCD to binary.
  95 = 1011111

## Slide 14: Error Codes: Cyclic Redundancy Check
Q6

## Slide 15: Error Codes: Cyclic Redundancy Check
A6

## Slide 16
Q&A

## Slide 17: Thank You!